## Slide 1
Computer Architecture
（计算机体系结构) Lecture 24 Introduction to CPU design 2020-10-16
Lecturer
Yuanqing Cheng

## Slide 2: Clever Signed Adder/Subtractor
A - B = A + (-B); how do we make “-B”?
x | y | xor
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
An xor is a “Conditional Inverter!”

## Slide 3: Five Components of a Computer
Processor
Computer
Control
Datapath
Memory
(passive)
(where
programs,
data live
when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Printer
Disk (where
programs,
data live when not running)

## Slide 4: The CPU
Processor (CPU): the active part of the computer, which does all the work (data manipulation and decision-making)
Datapath: portion of the processor which contains hardware necessary to perform operations required by the processor (the brawn)
Control: portion of the processor (also in hardware) which tells the datapath what needs to be done (the brain)

## Slide 5: Stages of the Datapath : Overview
Problem: a single, atomic block which “executes an instruction” (performs all necessary operations beginning with fetching the instruction) would be too bulky and inefficient
Solution: break up the process of “executing an instruction” into stages, and then connect the stages to create the whole datapath
  smaller stages are easier to design
  easy to optimize (change) one stage without touching the others

## Slide 6: Stages of the Datapath (1/5)
There is a wide variety of MIPS instructions: so what general steps do they have in common?
Stage 1: Instruction Fetch
  no matter what the instruction, the 32-bit instruction word must first be fetched from memory (the cache-memory hierarchy)
  also, this is where we Increment PC (that is, PC = PC + 4, to point to the next instruction: byte addressing so + 4)

## Slide 7: Stages of the Datapath (2/5)
Stage 2: Instruction Decode
  upon fetching the instruction, we next gather data from the fields (decode all necessary instruction data)
  first, read the opcode to determine instruction type and field lengths
  second, read in data from all necessary registers
    for add, read two registers
    for addi, read one register
    for jal, no reads necessary

## Slide 8: Stages of the Datapath (3/5)
Stage 3: ALU (Arithmetic-Logic Unit)
  the real work of most instructions is done here: arithmetic (+, -, *, /), shifting, logic (&, |), comparisons (slt)
  what about loads and stores?
    lw $t0, 40($t1)
    the address we are accessing in memory = the value in $t1 PLUS the value 40
    so we do this addition in this stage

## Slide 9: Stages of the Datapath (4/5)
Stage 4: Memory Access
  actually only the load and store instructions do anything during this stage; the others remain idle during this stage or skip it all together
  since these instructions have a unique step, we need this extra stage to account for them
  as a result of the cache system, this stage is expected to be fast

## Slide 10: Stages of the Datapath (5/5)
Stage 5: Register Write
  most instructions write the result of some computation into a register
  examples: arithmetic, logical, shifts, loads, slt
  what about stores, branches, jumps?
    don’t write anything into a register at the end
    these remain idle during this fifth stage or skip it all together

## Slide 11: Generic Steps of Datapath
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Reg.
Write
PC

## Slide 12: Datapath Walkthroughs (1/3)
add $r3,$r1,$r2 # r3 = r1+r2
  Stage 1: fetch this instruction, inc. PC
  Stage 2: decode to find it’s an add, then read registers $r1 and $r2
  Stage 3: add the two values retrieved in Stage 2
  Stage 4: idle (nothing to write to memory)
  Stage 5: write result of Stage 3 into register $r3

## Slide 13: Example: add Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
2
1
3
add r3, r1, r2
reg[1]+reg[2]
reg[2]
reg[1]
PC

## Slide 14: Datapath Walkthroughs (2/3)
slti $r3,$r1,17
  Stage 1: fetch this instruction, inc. PC
  Stage 2: decode to find it’s an slti, then read register $r1
  Stage 3: compare value retrieved in Stage 2 with the integer 17
  Stage 4: idle
  Stage 5: write the result of Stage 3 in register $r3

## Slide 15: Example: slti Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
3
1
x
slti r3, r1, 17
reg[1]<17?
17
reg[1]
PC

## Slide 16: Datapath Walkthroughs (3/3)
sw $r3, 17($r1)
  Stage 1: fetch this instruction, inc. PC
  Stage 2: decode to find it’s a sw, then read registers $r1 and $r3
  Stage 3: add 17 to value in register $r1 (retrieved in Stage 2)
  Stage 4: write value in register $r3 (retrieved in Stage 2) into memory address computed in Stage 3
  Stage 5: idle (nothing to write into a register)

## Slide 17: Example: sw Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
3
1
x
SW r3, 17(r1)
reg[1]+17
17
reg[1]
MEM[r1+17]<=r3
reg[3]
PC

## Slide 18: Why Five Stages? (1/2)
Could we have a different number of stages?
  Yes, and other architectures do
So why does MIPS have five if instructions tend to idle for at least one stage?
  The five stages are the union of all the operations needed by all the instructions.
  There is one instruction that uses all five stages: the load

## Slide 19: Why Five Stages? (2/2)
lw $r3, 17($r1)
  Stage 1: fetch this instruction, inc. PC
  Stage 2: decode to find it’s a lw, then read register $r1
  Stage 3: add 17 to value in register $r1 (retrieved in Stage 2)
  Stage 4: read value from memory address compute in Stage 3
  Stage 5: write value found in Stage 4 into register $r3

## Slide 20: Example: lw Instruction
ALU
instruction
memory
+4
registers
Data
memory
imm
3
1
x
LW r3, 17(r1)
reg[1]+17
17
reg[1]
MEM[r1+17]
PC

## Slide 21: Datapath Summary
The datapath based on data transfers required to perform instructions
A controller causes the right transfers to happen
PC
instruction
memory
+4
rt
rs
rd
registers
Data
memory
imm
ALU
Controller
opcode, funct

## Slide 22: What Hardware Is Needed? (1/2)
PC: a register which keeps track of memory addr of the next instruction
General Purpose Registers
  used in Stages 2 (Read) and 5 (Write)
  MIPS has 32 of these
Memory
  used in Stages 1 (Fetch) and 4 (R/W)
  cache system makes these two stages as fast as the others, on average

## Slide 23: What Hardware Is Needed? (2/2)
ALU
  used in Stage 3
  something that performs all necessary functions: arithmetic, logicals, etc.
  we’ll design details later
Miscellaneous Registers
  In implementations with only one stage per clock cycle, registers are inserted between stages to hold intermediate data and control signals as they travels from stage to stage.
  Note: Register is a general purpose term meaning something that stores bits. Not all registers are in the “register file”.

## Slide 24: CPU clocking (1/2)
Single Cycle CPU: All stages of an instruction are completed within one long clock cycle.
  The clock cycle is made sufficient long to allow each instruction to complete all stages without interruption and within one cycle.
For each instruction, how do we control the flow of information though the datapath?
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Reg.
Write

## Slide 25: CPU clocking (2/2)
Multiple-cycle CPU: Only one stage of instruction per clock cycle.
  The clock is made as long as the slowest stage.
  Several significant advantages over single cycle execution: Unused stages in a particular instruction can be skipped OR instructions can be pipelined (overlapped).
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Reg.
Write
For each instruction, how do we control the flow of information though the datapath?

## Slide 26: Peer Instruction
If the destination reg is the same as the source reg, we could compute the incorrect value!
We’re going to be able to read 2 registers and write a 3rd in 1 cycle
Datapath is hard, Control is easy
ABC
0: FFF
1: FFT
2: FTF
3: FTT
4: TFF
5: TFT
6: TTF
7: TTT
Notes: Answer: [correct=3, FTF]
A: F (waste of resources -- won’t work for pipelining)
B: T (yep!)
C: F (nope, that’s not our mantra silly)

## Slide 27: Peer Instruction
Truth table for mux with 4-bits of signals has 24 rows
We could cascade N 1-bit shifters to make 1 N-bit shifter for sll, srl
If 1-bit adder delay is T, the N-bit adder delay would also be T
ABC
1: FFF
2: FFT
3: FTF
4: FTT
5: TFF
6: TFT
7: TTF
8: TTT

## Slide 28: Peer Instruction Answer
Truth table for mux with 4-bits of signals is 24 rows long
We could cascade N 1-bit shifters to make 1 N-bit shifter for sll, srl
If 1-bit adder delay is T, the N-bit adder delay would also be T
ABC
1: FFF
2: FFT
3: FTF
4: FTT
5: TFF
6: TFT
7: TTF
8: TTT
Truth table for mux with 4-bits of signals controls 16 inputs, for a total of 20 inputs, so truth table is 220 rows…FALSE
We could cascade N 1-bit shifters to make 1 N-bit shifter for sll, srl … TRUE
What about the cascading carry? FALSE
Notes: Answer: [correct=5, TFF] Individual (6, 3, 6, 3, 34, 37, 7, 4)% & Team (9, 4, 4, 4, 39, 34, 0, 7)%
A: T [18/82 & 25/75] (The game breaks up very quickly into separate, independent games -- big win to solve separated & put together)
B: F [80/20 & 86/14] (The game tree grows exponentially! A better static evaluator can make all the difference!)
C: F [53/57 & 52/48] (If you're just looking for the best move, just keep theBestMove around [ala memoizing max])

## Slide 29: “And In conclusion…”
N-bit adder-subtractor done using N 1-bit adders with XOR gates on input
  XOR serves as conditional inverter
CPU design involves Datapath,Control
  Datapath in MIPS involves 5 CPU stages
    Instruction Fetch
    Instruction Decode & Register Read
    ALU (Execute)
    Memory
    Register Write