## Slide 1
Computer Architecture
（计算机体系结构) Lecture 23– CPU Design : Pipelining to Improve Performance 2020-10-23
Lecturer Yuanqing Cheng

## Slide 2: Review: Single cycle datapath
5 steps to design a processor
  Analyze instruction set  datapath requirements
  Select set of datapath components & establish clock methodology
  Assemble datapath meeting the requirements
  Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  Assemble the control logic
Control is the hard part
MIPS makes that easier
  Instructions same size
  Source registers always in same place
  Immediates same size, location
  Operations always on registers/immediates
Control
Datapath
Memory
Processor
Input
Output

## Slide 3: How We Build The Controller
RegDst = add + sub ALUSrc = ori + lw + sw MemtoReg = lw RegWrite = add + sub + ori + lw MemWrite = sw nPCsel = beq Jump = jump ExtOp = lw + sw ALUctr[0] = sub + beq (assume ALUctr is 0 ADD, 01: SUB, 10: OR) ALUctr[1] = or
where,
rtype = ~op5  ~op4  ~op3  ~op2  ~op1  ~op0, ori = ~op5  ~op4  op3  op2  ~op1  op0 lw = op5  ~op4  ~op3  ~op2  op1  op0 sw = op5  ~op4  op3  ~op2  op1  op0 beq = ~op5  ~op4  ~op3  op2  ~op1  ~op0 jump = ~op5  ~op4  ~op3  ~op2  op1  ~op0
add = rtype  func5  ~func4  ~func3  ~func2  ~func1  ~func0 sub = rtype  func5  ~func4  ~func3  ~func2  func1  ~func0
Omigosh omigosh,
do you know what this means?
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPCsel
Jump
ExtOp
ALUctr[0]
ALUctr[1]
“AND” logic
“OR” logic
opcode
func

## Slide 4: Call home, we’ve made HW/SW contact!
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g.,MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation

## Slide 5: Processor Performance
Can we estimate the clock rate (frequency) of our single-cycle processor? We know:
  1 cycle per instruction
  lw is the most demanding instruction.
  Assume these delays for major pieces of the datapath:
    Instr. Mem, ALU, Data Mem : 2ns each, regfile 1ns
    Instruction execution requires: 2 + 1 + 2 + 2 + 1 = 8ns
     125 MHz
What can we do to improve clock rate?
Will this improve performance as well?
  We want increases in clock rate to result in programs executing quicker.

## Slide 6: Gotta Do Laundry
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, fold, and put away
  Washer takes 30 minutes
  Dryer takes 30 minutes
  “Folder” takes 30 minutes
  “Stasher” takes 30 minutes to put clothes into drawers
A
B
C
D

## Slide 7: Sequential Laundry
Sequential laundry takes 8 hours for 4 loads
T
a
s
k
O
r
d
e
r
B
C
D
A
30
Time
30
30
30
30
30
30
30
30
30
30
30
30
30
30
30
6 PM
7
8
9
10
11
12
1
2 AM

## Slide 8: Pipelined Laundry
Pipelined laundry takes 3.5 hours for 4 loads!
T
a
s
k
O
r
d
e
r
B
C
D
A
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 9: General Definitions
Latency: time to completely execute a certain task
  for example, time to read a sector from disk is disk access time or disk latency
Throughput: amount of work that can be done over a period of time

## Slide 10: Pipelining Lessons (1/2)
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Time to “fill” pipeline and time to “drain” it reduces speedup: 2.3X v. 4X in this example
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 11: Pipelining Lessons (2/2)
Suppose new Washer takes 20 minutes, new Stasher takes 20 minutes. How much faster is pipeline?
Pipeline rate limited by slowest pipeline stage
Unbalanced lengths of pipe stages reduces speedup
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 12: Steps in Executing MIPS
1) IFtch: Instruction Fetch, Increment PC
2) Dcd: Instruction Decode, Read Registers
3) Exec: Mem-ref: Calculate Address Arith-log: Perform Operation
4) Mem: Load: Read Data from Memory Store: Write Data to Memory
5) WB: Write Data Back to Register

## Slide 13: Pipelined Execution Representation
Every instruction must take same number of steps, also called pipeline “stages”, so some will go idle sometimes
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
Time

## Slide 14: Review: Datapath for MIPS
Use datapath figure to represent pipeline
IFtch
Dcd
Exec
Mem
WB
ALU
I$
Reg
D$
Reg
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back

## Slide 15: Graphical Pipeline Representation
I
n
s
t
r.
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
(In Reg, right half highlight read, left half write)
Reg
I$

## Slide 16: Example
Suppose 2 ns for memory access, 2 ns for ALU operation, and 1 ns for register file read or write; compute instruction rate
Nonpipelined Execution:
  lw : IF + Read Reg + ALU + Memory + Write Reg = 2 + 1 + 2 + 2 + 1 = 8 ns
  add: IF + Read Reg + ALU + Write Reg = 2 + 1 + 2 + 1 = 6 ns (recall 8ns for single-cycle processor)
Pipelined Execution:
  Max(IF,Read Reg,ALU,Memory,Write Reg) = 2 ns

## Slide 17: Pipeline Hazard: Matching socks in later load
A depends on D; stall since folder tied up
T
a
s
k
O
r
d
e
r
B
C
D
A
E
F
bubble
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 18: Problems for Pipelining CPUs
Limits to pipelining: Hazards prevent next instruction from executing during its designated clock cycle
  Structural hazards: HW cannot support some combination of instructions (single person to fold and put clothes away)
  Control hazards: Pipelining of branches causes later instruction fetches to wait for the result of the branch
  Data hazards: Instruction depends on result of prior instruction still in the pipeline (missing sock)
These might result in pipeline stalls or “bubbles” in the pipeline.

## Slide 19: Structural Hazard #1: Single Memory (1/2)
Read same memory twice in same clock cycle
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 20: Structural Hazard #1: Single Memory (2/2)
Solution:
  infeasible and inefficient to create second memory
  (We’ll learn about this more next week)
  so simulate this by having two Level 1 Caches (a temporary smaller [of usually most recently used] copy of memory)
  have both an L1 Instruction Cache and an L1 Data Cache
  need more complex hardware to control when both caches miss

## Slide 21: Structural Hazard #2: Registers (1/2)
Can we read and write to registers simultaneously?
I$
sw
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 22: Structural Hazard #2: Registers (2/2)
Two different solutions have been used:
  1) RegFile access is VERY fast: takes less than half the time of ALU stage
    Write to Registers during first half of each clock cycle
    Read from Registers during second half of each clock cycle
  2) Build RegFile with independent read and write ports
Result: can perform Read and Write during same clock cycle

## Slide 23: Peer Instruction
Thanks to pipelining, I have reduced the time it took me to wash my one shirt.
Longer pipelines are always a win (since less work per stage & a faster clock).
12
a) FF
b) FT
c) TF
d) TT

## Slide 24: Peer Instruction Answer
Thanks to pipelining, I have reduced the time it took me to wash my one shirt.
Longer pipelines are always a win (since less work per stage & a faster clock).
F A L S E
F A L S E
Throughput better, not execution time
“…longer pipelines do usually mean faster clock, but branches cause problems!”
12
a) FF
b) FT
c) TF
d) TT

## Slide 25: Things to Remember
Optimal Pipeline
  Each stage is executing part of an instruction each clock cycle.
  One instruction finishes during each clock cycle.
  On average, execute far more quickly.
What makes this work?
  Similarities between instructions allow us to use same stages for all instructions (generally).
  Each stage takes about the same amount of time as all others: little wasted time.