## Slide 1
Computer Architecture
（计算机体系结构) Lecture 25 – CPU Design : Pipelining to Improve Performance II 2020-10-26
Lecturer Yuanqing Cheng

## Slide 2: Review
Pipelining is a BIG idea
Optimal Pipeline
  Each stage is executing part of an instruction each clock cycle.
  One instruction finishes during each clock cycle.
  On average, execute far more quickly.
What makes this work?
  Similarities between instructions allow us to use same stages for all instructions (generally).
  Each stage takes about the same amount of time as all others: little wasted time.

## Slide 3: Problems for Pipelining CPUs
Limits to pipelining: Hazards prevent next instruction from executing during its designated clock cycle
  Structural hazards: HW cannot support some combination of instructions (single person to fold and put clothes away)
  Control hazards: Pipelining of branches causes later instruction fetches to wait for the result of the branch
  Data hazards: Instruction depends on result of prior instruction still in the pipeline (missing sock)
These might result in pipeline stalls or “bubbles” in the pipeline.

## Slide 4: Structural Hazard #1: Single Memory (1/2)
Read same memory twice in same clock cycle
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 5: Structural Hazard #1: Single Memory (2/2)
Solution:
  infeasible and inefficient to create second memory
  (We’ll learn about this shortly)
  …so simulate this by having two Level 1 Caches
    (a temporary smaller [of usually most recently used] copy of memory)
  have both an L1 Instruction Cache and an L1 Data Cache
  need more complex hardware to control when both caches miss

## Slide 6: Structural Hazard #2: Registers (1/2)
Can we read and write to registers simultaneously?
I$
sw
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 7: Structural Hazard #2: Registers (2/2)
Two different solutions have been used:
  1) RegFile access is VERY fast: takes less than half the time of ALU stage
    Write to Registers during first half of each clock cycle
    Read from Registers during second half of each clock cycle
  2) Build RegFile with independent read and write ports
Result: can perform Read and Write during same clock cycle

## Slide 8: Control Hazard: Branching (1/9)
Where do we do the compare for the branch?
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 9: Control Hazard: Branching (2/9)
We had put branch decision-making hardware in ALU stage
  therefore two more instructions after the branch will always be fetched, whether or not the branch is taken
Desired functionality of a branch
  if we do not take the branch, don’t waste any time and continue executing normally
  if we take the branch, don’t execute any instructions after the branch, just go to the desired label

## Slide 10: Control Hazard: Branching (3/9)
Initial Solution: Stall until decision is made
  insert “no-op” instructions (those that accomplish nothing, just take time) or hold up the fetch of the next instruction (for 2 cycles).
  Drawback: branches take 3 clock cycles each (assuming comparator is put in ALU stage)

## Slide 11: Control Hazard: Branching (4/9)
Optimization #1:
  insert special branch comparator in Stage 2
  as soon as instruction is decoded (Opcode identifies it as a branch), immediately make a decision and set the new value of the PC
  Benefit: since branch is complete in Stage 2, only one unnecessary instruction is fetched, so only one no-op is needed
  Side Note: This means that branches are idle in Stages 3, 4 and 5.

## Slide 12: Control Hazard: Branching (5/9)
Branch comparator moved to Decode stage.
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 13: Control Hazard: Branching (6/9)
User inserting no-op instruction
add
beq
nop
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
I$
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
bubble
Impact: 2 clock cycles per branch instruction  slow
lw
bubble
bubble
bubble
bubble

## Slide 14: Control Hazard: Branching (7/9)
Controller inserting a single bubble
add
beq
lw
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
I$
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
bubble
Impact: 2 clock cycles per branch instruction  slow
…story about engineer, physicist, mathematician asked to build a fence around a flock of sheep using minimal fence…
Notes: An engineer, a physicist and a mathematicians have to build a fence around
a flock of sheep, using as little material as possible.
The engineer forms the flock into a circular shape and constructs a fence
around it.
The physicist builds a fence with an infinite diameter and pulls it together
until it fits around the flock.
The mathematicians thinks for a while, then builds a fence around himself
and defines himself as being outside.
SUMMARY? Redefine the problem!

## Slide 15: Control Hazard: Branching (8/9)
Optimization #2: Redefine branches
  Old definition: if we take the branch, none of the instructions after the branch get executed by accident
  New definition: whether or not we take the branch, the single instruction immediately following the branch gets executed (called the branch-delay slot)
The term “Delayed Branch” means we always execute inst after branch
This optimization is used with MIPS

## Slide 16: Control Hazard: Branching (9/9)
Notes on Branch-Delay Slot
  Worst-Case Scenario: can always put a no-op in the branch-delay slot
  Better Case: can find an instruction preceding the branch which can be placed in the branch-delay slot without affecting flow of the program
    re-ordering instructions is a common method of speeding up programs
    compiler must be very smart in order to find instructions to do this
    usually can find such an instruction at least 50% of the time
    Jumps also have a delay slot…

## Slide 17: Example: Nondelayed vs. Delayed Branch
add $1 ,$2,$3
sub $4, $5,$6
beq $1, $4, Exit
or $8, $9 ,$10
xor $10, $1,$11
Nondelayed Branch
add $1 ,$2,$3
sub $4, $5,$6
beq $1, $4, Exit
or $8, $9 ,$10
xor $10, $1,$11
Delayed Branch
Exit:
Exit:

## Slide 18: Data Hazards (1/2)
Consider the following sequence of instructions
add $t0, $t1, $t2
sub $t4, $t0 ,$t3
and $t5, $t0 ,$t6
or $t7, $t0 ,$t8
xor $t9, $t0 ,$t10

## Slide 19: Data Hazards (2/2)
Data-flow backward in time are hazards
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 20: Data Hazard Solution: Forwarding
Forward result from one stage to another
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
“or” hazard solved by register hardware

## Slide 21: Data Hazard: Loads (1/4)
Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
Must stall instruction dependent on load, then forward (more hardware)
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
lw $t0,0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 22: Data Hazard: Loads (2/4)
Hardware stalls pipeline
  Called “interlock”
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
bubble
and $t5,$t0,$t4
ALU
I$
Reg
D$
Reg
bubble
or $t7,$t0,$t6
I$
ALU
Reg
D$
bubble
lw $t0, 0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 23: Data Hazard: Loads (3/4)
Instruction slot after a load is called “load delay slot”
If that instruction uses the result of the load, then the hardware interlock will stall it for one cycle.
If the compiler puts an unrelated instruction in that slot, then no stall
Letting the hardware stall the instruction in the delay slot is equivalent to putting a nop in the slot (except the latter uses more code space)

## Slide 24: Data Hazard: Loads (4/4)
Stall is equivalent to nop
sub $t3,$t0,$t2
and $t5,$t0,$t4
or $t7,$t0,$t6
I$
ALU
Reg
D$
lw $t0, 0($t1)
ALU
I$
Reg
D$
Reg
bubble
bubble
bubble
bubble
bubble
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
nop

## Slide 25: Peer Instruction
Thanks to pipelining, I have reduced the time it took me to wash my one shirt.
Longer pipelines are always a win (since less work per stage & a faster clock).
12
a) FF
b) FT
c) TF
d) TT

## Slide 26: “And in Conclusion..”
Pipeline challenge is hazards
  Forwarding helps w/many data hazards
  Delayed branch helps with control hazard in 5 stage pipeline
  Load delay slot / interlock necessary
More aggressive performance:
  Superscalar
  Out-of-order execution

## Slide 27: Bonus slides
These are extra slides that used to be included in lecture notes, but have been moved to this, the “bonus” area to serve as a supplement.
The slides will appear in the order they would have in the normal presentation
Bonus

## Slide 28: Historical Trivia
First MIPS design did not interlock and stall on load-use data hazard
Real reason for name behind MIPS: Microprocessor without Interlocked Pipeline Stages
  Word Play on acronym for Millions of Instructions Per Second, also called MIPS

## Slide 29: Pipeline Hazard: Matching socks in later load
A depends on D; stall since folder tied up; Note this is much different from processor cases so far. We have not had a earlier instruction depend on a later one.
T
a
s
k
O
r
d
e
r
B
C
D
A
E
F
bubble
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 30: Out-of-Order Laundry: Don’t Wait
A depends on D; rest continue; need more resources to allow out-of-order
T
a
s
k
O
r
d
e
r
12
2 AM
6 PM
7
8
9
10
11
1
Time
B
C
D
A
30
30
30
30
30
30
30
E
F
bubble

## Slide 31: Superscalar Laundry: Parallel per stage
More resources, HW to match mix of parallel tasks?
T
a
s
k
O
r
d
e
r
12
2 AM
6 PM
7
8
9
10
11
1
Time
B
C
D
A
E
F
(light clothing)
(dark clothing)
(very dirty clothing)
(light clothing)
(dark clothing)
(very dirty clothing)
30
30
30
30
30

## Slide 32: Superscalar Laundry: Mismatch Mix
Task mix underutilizes extra resources
T
a
s
k
O
r
d
e
r
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30
(light clothing)
(light clothing)
(dark clothing)
(light clothing)
A
B
D
C

## Slide 33: Peer Instruction (1/2)
Assume 1 instr/clock, delayed branch, 5 stage pipeline, forwarding, interlock on unresolved load hazards (after 103 loops, so pipeline full)
Loop: lw $t0, 0($s1) addu $t0, $t0, $s2 sw $t0, 0($s1) addiu $s1, $s1, -4 bne $s1, $zero, Loop nop
How many pipeline stages (clock cycles) per loop iteration to execute this code?
1
2
3
4
5
6
7
8
9
10

## Slide 34: Peer Instruction Answer (1/2)
Assume 1 instr/clock, delayed branch, 5 stage pipeline, forwarding, interlock on unresolved load hazards. 103 iterations, so pipeline full.
Loop: lw $t0, 0($s1) addu $t0, $t0, $s2 sw $t0, 0($s1) addiu $s1, $s1, -4 bne $s1, $zero, Loop nop
How many pipeline stages (clock cycles) per loop iteration to execute this code?
1.
2. (data hazard so stall)
3.
4.
5.
6.
(delayed branch so exec. nop)
7.
1 2 3 4 5 6 7 8 9 10

## Slide 35: Peer Instruction (2/2)
Assume 1 instr/clock, delayed branch, 5 stage pipeline, forwarding, interlock on unresolved load hazards (after 103 loops, so pipeline full). Rewrite this code to reduce pipeline stages (clock cycles) per loop to as few as possible.
Loop: lw $t0, 0($s1) addu $t0, $t0, $s2 sw $t0, 0($s1) addiu $s1, $s1, -4 bne $s1, $zero, Loop nop
How many pipeline stages (clock cycles) per loop iteration to execute this code?
1
2
3
4
5
6
7
8
9
10

## Slide 36: Peer Instruction (2/2) How long to execute?
How many pipeline stages (clock cycles) per loop iteration to execute your revised code? (assume pipeline is full)
Rewrite this code to reduce clock cycles per loop to as few as possible:
Loop: lw $t0, 0($s1) addiu $s1, $s1, -4 addu $t0, $t0, $s2 bne $s1, $zero, Loop sw $t0, +4($s1)
(no hazard since extra cycle)
1.
3.
4.
5.
2.
(modified sw to put past addiu)
1 2 3 4 5 6 7 8 9 10