## Slide 1
Computer Architecture
（计算机体系结构) Lecture 25 – Caches I 2020-10-26
Lecturer: Yuanqing Cheng

## Slide 2: Review : Pipelining
Pipeline challenge is hazards
  Forwarding helps w/many data hazards
  Delayed branch helps with control hazard in our 5 stage pipeline
  Data hazards w/Loads → Load Delay Slot
    Interlock →“smart” CPU has HW to detect if conflict with inst following load, if so it stalls
More aggressive performance (discussed in section next week)
  Superscalar (parallelism)
  Out-of-order execution

## Slide 3: The Big Picture
Processor
(active)
Computer
Control
(“brain”)
Datapath
(“brawn”)
Memory
(passive)
(where
programs,
data live
when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Printer
Disk,
Network

## Slide 4: Memory Hierarchy
Processor
  holds data in register file (~100 Bytes)
  Registers accessed on nanosecond timescale
Memory (we’ll call “main memory”)
  More capacity than registers (~Gbytes)
  Access time ~50-100 ns
  Hundreds of clock cycles per memory access?!
Disk
  HUGE capacity (virtually limitless)
  VERY slow: runs ~milliseconds
I.e., storage in computer systems

## Slide 5: Motivation: Why We Use Caches (written $)
1989 first Intel CPU with cache on chip
1998 Pentium III has two cache levels on chip
µProc
60%/yr.
DRAM
7%/yr.
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (grows 50% / year)
Performance
Notes: Y-axis is performance
X-axis is time
Latency
Cliché:
Not e that x86 didn’t have cache on chip until 1989

## Slide 6: Memory Caching
Mismatch between processor and memory speeds leads us to add a new level: a memory cache
Implemented with same IC processing technology as the CPU (usually integrated on same chip): faster but more expensive than DRAM memory.
Cache is a copy of a subset of main memory.
Most processors have separate caches for instructions and data.

## Slide 7: Memory Hierarchy
Processor
Size of memory at each level
Increasing Distance from Proc., Decreasing speed
Level 1
Level 2
Level n
Level 3
. . .
Higher
Lower
Levels in memory hierarchy
As we move to deeper levels the latency goes up and price per bit goes down.

## Slide 8: Memory Hierarchy
If level closer to Processor, it is:
  Smaller
  Faster
  More expensive
  subset of lower levels (contains most recently used data)
Lowest Level (usually disk) contains all available data (does it go beyond the disk?)
Memory Hierarchy presents the processor with the illusion of a very large & fast memory

## Slide 9: Memory Hierarchy Analogy: Library (1/2)
You’re writing a term paper (Processor) at a table in Doe
Doe Library is equivalent to disk
  essentially limitless capacity
  very slow to retrieve a book
Table is main memory
  smaller capacity: means you must return book when table fills up
  easier and faster to find a book there once you’ve already retrieved it

## Slide 10: Memory Hierarchy Analogy: Library (2/2)
Open books on table are cache
  smaller capacity: can have very few open books fit on table; again, when table fills up, you must close a book
  much, much faster to retrieve data
Illusion created: whole library open on the tabletop
  Keep as many recently used books open on table as possible since likely to use again
  Also keep as many books on table as possible, since faster than going to library

## Slide 11: Memory Hierarchy Basis
Cache contains copies of data in memory that are being used.
Memory contains copies of data on disk that are being used.
Caches work on the principles of temporal and spatial locality.
  Temporal Locality: if we use it now, chances are we’ll want to use it again soon.
  Spatial Locality: if we use a piece of memory, chances are we’ll use the neighboring pieces soon.

## Slide 12: Cache Design
How do we organize cache?
Where does each memory address map to?
  (Remember that cache is subset of memory, so multiple memory addresses map to the same cache location.)
How do we know which elements are in cache?
How do we quickly locate them?

## Slide 13: Direct-Mapped Cache (1/4)
In a direct-mapped cache, each memory address is associated with one possible block within the cache
  Therefore, we only need to look in a single location in the cache for the data if it exists in the cache
  Block is the unit of transfer between cache and memory

## Slide 14: Direct-Mapped Cache (2/4)
Cache Location 0 can be occupied by data from:
  Memory location 0, 4, 8, ...
  4 blocks any memory location that is multiple of 4
Memory
Memory Address
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
4 Byte Direct
Mapped Cache
Cache
Index
0
1
2
3
What if we wanted a block to be bigger than one byte?
Block size = 1 byte
Notes: Let’s look at the simplest cache one can build. A direct mapped cache that only has 4 bytes.
In this direct mapped cache with only 4 bytes, location 0 of the cache can be occupied by data form memory location 0, 4, 8, C, ... and so on.
While location 1 of the cache can be occupied by data from memory location 1, 5, 9, ... etc.
So in general, the cache location where a memory location can map to is uniquely determined by the 2 least significant bits of the address (Cache Index).
For example here, any memory location whose two least significant bits of the address are 0s can go to cache location zero.
With so many memory locations to chose from, which one should we place in the cache?
Of course, the one we have read or write most recently because by the principle of temporal locality, the one we just touch is most likely to be the one we will need again soon.
Of all the possible memory locations that can be placed in cache Location 0, how can we tell which one is in the cache?
+2 = 22 min. (Y:02)

## Slide 15: Direct-Mapped Cache (3/4)
When we ask for a byte, the system finds out the right block, and loads it all!
  How does it know right block?
  How do we select the byte?
E.g., Mem address 11101?
How does it know WHICH colored block it originated from?
  What do you do at baggage claim?
Memory
Memory Address
0
2
4
6
8
A
C
E
10
12
14
16
18
1A
1C
1E
8 Byte Direct
Mapped Cache
Cache
Index
0
1
2
3
0
1
2
3
etc
Block size = 2 bytes
4
5
6
7
8
9
Notes: Let’s look at the simplest cache one can build. A direct mapped cache that only has 4 bytes.
In this direct mapped cache with only 4 bytes, location 0 of the cache can be occupied by data form memory location 0, 4, 8, C, ... and so on.
While location 1 of the cache can be occupied by data from memory location 1, 5, 9, ... etc.
So in general, the cache location where a memory location can map to is uniquely determined by the 2 least significant bits of the address (Cache Index).
For example here, any memory location whose two least significant bits of the address are 0s can go to cache location zero.
With so many memory locations to chose from, which one should we place in the cache?
Of course, the one we have read or write most recently because by the principle of temporal locality, the one we just touch is most likely to be the one we will need again soon.
Of all the possible memory locations that can be placed in cache Location 0, how can we tell which one is in the cache?
+2 = 22 min. (Y:02)

## Slide 16: Direct-Mapped Cache (4/4)
What should go in the tag?
  Do we need the entire address?
    What do all these tags have in common?
  What did we do with the immediate when we were branch addressing, always count by bytes?
Why not count by cache #?
  It’s useful to draw memory with the same width as the block size
Memory
(addresses shown)
Memory Address
0
2
4
6
8
A
C
E
10
12
14
16
18
1A
1C
1E
8 Byte Direct
Mapped Cache w/Tag!
Cache
Index
0
1
2
3
0
1
2
3
etc
Tag Data
(Block size = 2 bytes)
4
5
6
7
8
9
8
2
1E
14
0
1
2
3
Cache#
1
0
3
2
Notes: Let’s look at the simplest cache one can build. A direct mapped cache that only has 4 bytes.
In this direct mapped cache with only 4 bytes, location 0 of the cache can be occupied by data form memory location 0, 4, 8, C, ... and so on.
While location 1 of the cache can be occupied by data from memory location 1, 5, 9, ... etc.
So in general, the cache location where a memory location can map to is uniquely determined by the 2 least significant bits of the address (Cache Index).
For example here, any memory location whose two least significant bits of the address are 0s can go to cache location zero.
With so many memory locations to chose from, which one should we place in the cache?
Of course, the one we have read or write most recently because by the principle of temporal locality, the one we just touch is most likely to be the one we will need again soon.
Of all the possible memory locations that can be placed in cache Location 0, how can we tell which one is in the cache?
+2 = 22 min. (Y:02)

## Slide 17: Issues with Direct-Mapped
Since multiple memory addresses map to same cache index, how do we tell which one is in there?
What if we have a block size > 1 byte?
Answer: divide memory address into three fields
ttttttttttttttttt iiiiiiiiii oooo
tag index byte to check to offset if have select within correct block block block

## Slide 18: Direct-Mapped Cache Terminology
All fields are read as unsigned integers.
Index
  specifies the cache index (which “row”/block of the cache we should look in)
Offset
  once we’ve found correct block, specifies which byte within the block we want
Tag
  the remaining bits after offset and index are determined; these are used to distinguish between all the memory addresses that map to the same location

## Slide 19: TIO great cache mnemonic
AREA (cache size, B) = HEIGHT (# of blocks) * WIDTH (size of one block, B/block)
WIDTH (size of one block, B/block)
HEIGHT (# of blocks)
AREA (cache size, B)
2(H+W) = 2H * 2W
Tag Index Offset

## Slide 20: Direct-Mapped Cache Example (1/3)
Suppose we have a 8B of data in a direct-mapped cache with 2 byte blocks
  Sound familiar?
Determine the size of the tag, index and offset fields if we’re using a 32-bit architecture
Offset
  need to specify correct byte within a block
  block contains 2 bytes
    = 21 bytes
  need 1 bit to specify correct byte

## Slide 21: Direct-Mapped Cache Example (2/3)
Index: (~index into an “array of blocks”)
  need to specify correct block in cache
  cache contains 8 B = 23 bytes
  block contains 2 B = 21 bytes
  # blocks/cache
    = bytes/cache bytes/block
    = 23 bytes/cache 21 bytes/block
    = 22 blocks/cache
  need 2 bits to specify this many blocks

## Slide 22: Direct-Mapped Cache Example (3/3)
Tag: use remaining bits as tag
  tag length = addr length – offset - index = 32 - 1 - 2 bits = 29 bits
  so tag is leftmost 29 bits of memory address
Why not full 32 bit address as tag?
  All bytes within block need same address (4b)
  Index must be same for every address within a block, so it’s redundant in tag check, thus can leave off to save memory (here 12 bits)

## Slide 23: And in Conclusion…
We would like to have the capacity of disk at the speed of the processor: unfortunately this is not feasible.
So we create a memory hierarchy:
  each successively lower level contains “most used” data from next higher level
  exploits temporal & spatial locality
  do the common case fast, worry less about the exceptions (design principle of MIPS)
Locality of reference is a Big Idea