## Slide 1
Computer Architecture
（计算机体系结构) Lecture 27 – Caches II 2020-10-30
Lecturer Yuanqing Cheng

## Slide 2: Direct-Mapped Cache Terminology
All fields are read as unsigned integers.
Index
  specifies the cache index (or “row”/block)
Tag
  distinguishes betw the addresses that map to the same location
Offset
  specifies which byte within the block we want
ttttttttttttttttt iiiiiiiiii oooo
tag index byte to check to offset if have select within correct block block block

## Slide 3: TIO Dan’s great cache mnemonic
AREA (cache size, B) = HEIGHT (# of blocks) * WIDTH (size of one block, B/block)
WIDTH (size of one block, B/block)
HEIGHT (# of blocks)
AREA (cache size, B)
2(H+W) = 2H * 2W
Tag Index Offset
Addr size (usu 32 bits)

## Slide 4: Caching Terminology
When reading memory, 3 things can happen:
  cache hit: cache block is valid and contains proper address, so read desired word
  cache miss: nothing in cache in appropriate block, so fetch from memory
  cache miss, block replacement: wrong data is in cache at appropriate block, so discard it and fetch desired data from memory (cache always copy)

## Slide 5: Accessing data in a direct mapped cache
Ex.: 16KB of data, direct-mapped, 4 word blocks
  Can you work out height, width, area?
Read 4 addresses
  0x00000014
  0x0000001C
  0x00000034
  0x00008014
Memory vals here:
Address (hex)
Value of Word
Memory
00000010
00000014
00000018
0000001C
a
b
c
d
...
...
00000030
00000034
00000038
0000003C
e
f
g
h
00008010
00008014
00008018
0000801C
i
j
k
l
...
...
...
...
...
...

## Slide 6: Accessing data in a direct mapped cache
4 Addresses:
  0x00000014, 0x0000001C, 0x00000034, 0x00008014
4 Addresses divided (for convenience) into Tag, Index, Byte Offset fields
000000000000000000 0000000001 0100
000000000000000000 0000000001 1100
000000000000000000 0000000011 0100
000000000000000010 0000000001 0100 Tag Index Offset

## Slide 7: 16 KB Direct Mapped Cache, 16B blocks
Valid bit: determines whether anything is stored in that row (when computer initially turned on, all entries invalid)
...
Valid
Tag
0xc-f
0x8-b
0x4-7
0x0-3
0
1
2
3
4
5
6
7
1022
1023
...
Index
0
0
0
0
0
0
0
0
0
0

## Slide 8: 1. Read 0x00000014
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
000000000000000000 0000000001 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3

## Slide 9: So we read block 1 (0000000001)
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
000000000000000000 0000000001 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3

## Slide 10: No valid data
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
000000000000000000 0000000001 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3

## Slide 11: So load that data into cache, setting tag, valid
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
d
c
b
a
000000000000000000 0000000001 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3

## Slide 12: Read from cache at offset, return word b
000000000000000000 0000000001 0100
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 13: 2. Read 0x0000001C = 0…00 0..001 1100
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000001 1100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 14: Index is Valid
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000001 1100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 15: Index valid, Tag Matches
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000001 1100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 16: Index Valid, Tag Matches, return d
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000001 1100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 17: 3. Read 0x00000034 = 0…00 0..011 0100
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000011 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 18: So read block 3
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000011 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 19: No valid data
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000011 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 20: Load that cache block, return word f
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000011 0100
1
0
h
g
f
e
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
d
c
b
a
0xc-f
0x8-b
0x4-7
0x0-3

## Slide 21: 4. Read 0x00008014 = 0…10 0..001 0100
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000010 0000000001 0100
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a
h
g
f
e

## Slide 22: So read Cache Block 1, Data is Valid
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000010 0000000001 0100
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a
h
g
f
e

## Slide 23: Cache Block 1 Tag does not match (0 != 2)
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000010 0000000001 0100
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a
h
g
f
e

## Slide 24: Miss, so replace block 1 with new data & tag
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
2
l
k
j
i
000000000000000010 0000000001 0100
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
h
g
f
e

## Slide 25: And return word J
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
2
000000000000000010 0000000001 0100
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
l
k
j
i
0xc-f
0x8-b
0x4-7
0x0-3
h
g
f
e

## Slide 26: Do an example yourself. What happens?
Chose from: Cache: Hit, Miss, Miss w. replace Values returned: a ,b, c, d, e, ..., k, l
Read address 0x00000030 ? 000000000000000000 0000000011 0000
Read address 0x0000001c ? 000000000000000000 0000000001 1100
...
Valid
Tag
0xc-f
0x8-b
0x4-7
0x0-3
0
1
2
3
4
5
6
7
...
1
2
l
k
j
i
1
0
h
g
f
e
Index
0
0
0
0
0
0
Cache

## Slide 27: Answers
0x00000030 a hit
  Index = 3, Tag matches, Offset = 0, value = e
0x0000001c a miss
  Index = 1, Tag mismatch, so replace from memory, Offset = 0xc, value = d
Since reads, values must = memory values whether or not cached:
  0x00000030 = e
  0x0000001c = d
Address (hex)
Value of Word
Memory
00000010
00000014
00000018
0000001C
a
b
c
d
...
...
00000030
00000034
00000038
0000003C
e
f
g
h
00008010
00008014
00008018
0000801C
i
j
k
l
...
...
...
...
...
...

## Slide 28: Peer Instruction
  Mem hierarchies were invented before 1950. (UNIVAC I wasn’t delivered ‘til 1951)
  If you know your computer’s cache size, you can often make your code run faster.
12
a) FF
b) FT
c) TF
d) TT

## Slide 29: Peer Instruction Answer
  “We are…forced to recognize the possibility of constructing a hierarchy of memories, each of which has greater capacity than the preceding but which is less accessible.” – von Neumann, 1946
  Certainly! That’s call “tuning”
12
a) FF
b) FT
c) TF
d) TT
  Mem hierarchies were invented before 1950. (UNIVAC I wasn’t delivered ‘til 1951)
  If you know your computer’s cache size, you can often make your code run faster.

## Slide 30: Peer Instruction
All caches take advantage of spatial locality.
All caches take advantage of temporal locality.
12
a) FF
b) FT
c) TF
d) TT
Notes: Answer: [correct=5, TFF] Individual (6, 3, 6, 3, 34, 37, 7, 4)% & Team (9, 4, 4, 4, 39, 34, 0, 7)%
A: T [18/82 & 25/75] (The game breaks up very quickly into separate, independent games -- big win to solve separated & put together)
B: F [80/20 & 86/14] (The game tree grows exponentially! A better static evaluator can make all the difference!)
C: F [53/57 & 52/48] (If you're just looking for the best move, just keep theBestMove around [ala memoizing max])

## Slide 31: Peer Instruction Answer
12
a) FF
b) FT
c) TF
d) TT
All caches take advantage of spatial locality.
All caches take advantage of temporal locality.
T R U E
F A L S E
Block size = 1, no spatial!
That’s the idea of caches; We’ll need it again soon.
All caches take advantage of spatial locality.
All caches take advantage of temporal locality.
Notes: Answer: [correct=5, TFF] Individual (6, 3, 6, 3, 34, 37, 7, 4)% & Team (9, 4, 4, 4, 39, 34, 0, 7)%
A: T [18/82 & 25/75] (The game breaks up very quickly into separate, independent games -- big win to solve separated & put together)
B: F [80/20 & 86/14] (The game tree grows exponentially! A better static evaluator can make all the difference!)
C: F [53/57 & 52/48] (If you're just looking for the best move, just keep theBestMove around [ala memoizing max])

## Slide 32: And in Conclusion…
Mechanism for transparent movement of data among levels of a storage hierarchy
  set of address/value bindings
  address  index to set of candidates
  compare desired address with tag
  service hit or miss
    load new block and binding on miss
Valid
Tag
0xc-f
0x8-b
0x4-7
0x0-3
0
1
2
3
...
1
0
d
c
b
a
000000000000000000 0000000001 1100
address: tag index offset